## Slide 1: ST25SDK (ST25 Software Development Kit)
Architecture overview document v1.0
August 11th 2017 MDG/MMY RFID Application Ecosystem team

## Slide 2: ST25SDK Requirements
Support of several readers with the same application (reuse of UI developments)
Software library to be used in Java applications
  Can be run any platform supporting JVM (Windows, Android, Linux)
  MacOs under reviewed
  iOs some components can be re-used.
Easy-to-use model of RF tags, including ST’s specific features
  Supports all features of new tags from ST25 family
  Supports all ST portfolio and generic Iso/NFC tags

## Slide 3: ST25SDK Requirements
Useful to different types of users:
  Industrial/commercial multi-tag applications
  Smartphone single tag applications
  Tag validation
Ability to share source code with customers
  Delivered as Java .jar library or
  Source code available through Mix MyLiberty License:
    Allows to share ST source code
    Delivers library for 3rd party software (crypto, etc)

## Slide 4: Architecture/Design Requirements
Quick to update for new products
    New tags
    New readers
Object oriented development
    Structure code around tags and readers
      Global reader instance whose properties get updated throughout the lifetime of the application
      Global tag instance updated throughout the lifetime of a RF or I2C session
    Tags have common properties
      Specific fields and methods for tags that have extra features or different from base tags
      We do not reinvent the wheel every time, just add or override fields and methods
    Inherit features based on tag hierarchy
Cross platforms/readers support
Easy to sandbox from SDK an ST tag
Cache tag information (useful when RF field is OFF)

## Slide 5: ST25SDK ARCHITECTURE
Overview

## Slide 6: Architecture overview
NDEF
NFC Forum
ISO 14443/15693
Custom
ST25TA02K
ST25DV
M24LR64E
RF Reader Interface
Commands
Tags
Ndef records
Reader implementation(s) based on Interface template
Application accesses the ST25SDK library through several APIs
used by
implements
called
by
instantiates
instantiates
instantiates
uses
Helper
classes
Helper
TagHelper
called
by
Low Level API
High Level API

## Slide 7: API Layers
API levels:
  Commands (low)
  Tags (highest)
  Ndef
  Readers
An application using the ST25SDK must:
  Instantiate a Command class object to access RF command methods OR
  Instantiate a NFCTag object to access generic and tag-specific methods OR
  Instantiate an Ndef class
The RF reader interface must
  Provide at least one reader implementation, used for Command and Tag layers
Commands
App
reader n
App reader 2
App
reader 1
Application
Ndef
RF Reader interface
SDK
Tags
Java layers
Java/C/C++ layers

## Slide 8: Command API
RF commands:
  Low level RF commands, very close to standards and datasheets
  Easy to work with multiple tags
  Very little extra processing
Commands are separated in
  Ndef commands calling on unitary commands
  Unitary commands corresponding to:
    NFC Forum RF commands from specifications
    Iso14443/15693 commands from specifications
    Tag-specific commands from datasheet
    Iso7816 commands from specifications
Unitary commands
Application
Reader Interface
Reader Implementation

## Slide 9: Tag API
The Tag API is the highest level of API to work with a single tag
  It contains the supported RF commands
  High level commands are also available, such as readBlocks() that will manage reading through areas, using readMultiple commands when supported, etc.
TODO: Explain inheritance hierarchy:
  NFCTag -> Type5Tag -> STType5Tag -> STType5MultiAreaTag-> ST25DVTag
Tags are implemented in the application based on the product identified using a SDK helper command
  Example:
    productName = TagHelper.identifyProduct(readerInterface, uid); switch (productName) {
    case PRODUCT_ST_ST25TA02K:
    recognizedTag = new ST25TA02KTag(readerInterface, uid);
    break;
    case PRODUCT_ST_ST25TA16K:
    recognizedTag = new ST25TA16KTag(readerInterface, uid);
    break;

## Slide 10: Ndef API
The Ndef API allow
  To parse NDEF from raw bytes
  To create/edit/read/write NDEF with well known records
  To manage multiple records
It is used by ST25 tags but can also be used to address multiple tags simultaneously

## Slide 11: RF Reader Interface
The RF reader interface can be seen as the porting layer of the ST25SDK. Each reader must implement the SDK’s readerInterface methods
Some examples of implementation are delivered with the SDK: Android, CR95HF, ST253911 and Feig
ret transceiver(data)
decodeTypeTag(uid)
Android app
Impl. reader n
Impl. reader 2
Impl. reader 1
PC Java app
SDK
RF Reader interface

## Slide 12: Architecture overview
The split in different isolated layers allows:
  To fully reuse an application on different platforms (e.g. the new ST25PC application run on Windows, Linux with different readers)
  To reuse a reader implementation for different applications (e.g. the RF reader implementation for CR95HF is used by different UI applications)
  To isolate and easily reuse some layers (e.g. the NDEF layer is used on iOs)

## Slide 13: ST25SDK DESIGN
V0.5.5

## Slide 14: SDK Code Organization
ST25 SDK is made of several java packages
st25sdk root folder contains:
  st25sdk.command:
  st25sdk.ndef
  st25sdk.type5
  st25sdk.type4A
  iso14443SR
st25sdk build is a jar library
RF Reader interface implementations delivered with SDK (for ST253911B, CR95HF and Feig) are made of java classes and java native interface in C/C++. For Android, the SDK is used.

## Slide 15: Class Hierarchy
UML graphs delivered with the Javadoc explain class hierarchy Example for Type5Tag:

## Slide 16: Tag Cache
An internal cache system allows to keep tag information when the tag is not in the reader field
Each tag has a cache in which object members (implementing or not the cache interface) can be added/removed

## Slide 17: Android/iOS Support
Android:
  The RF reader interface implementation is directly plugged on Android SDK APIs making it thin.
iOs:
  A tool named j2objc to convert the ST25SDK Java code to Objective C:
  « J2ObjC is an open-source command-line tool from Google that translates Java source code to Objective-C for the iOS (iPhone/iPad) platform. »
  Ndef package of ST25SDK is re-used for the ST25 iOs application

## Slide 18: Professional readers Support
ST253911B:
  The RF reader interface implementation is done through jni classes C/C++
  Build with gcc on Windows (no support so far on Linux)
CR95HF
  The RF reader interface implementation is done through jni classes C/C++
  Build with gcc on Windows and Linux with usb-hid backend
Feig:
  The RF reader interface implementation is done in java with proprietary classes delivered by Feig

## Slide 19: Open Source strategy
All the code source is available on st25.com